## Slide 1
University of Toronto Faculty of Applied Science and Engineering
Engineering Science Thesis
Sleep staging AI model design and ASIC implementation
Weekly progress log
Tristan Robitaille (EngSci 2T3 + PEY) Supervisor: Prof. Xilin Liu (X-Lab)
Fall 2023 – Winter 2024

## Slide 2
Tried | Will try
Unbiasing the dataset Clip lengths of 3.25s, 7.5s, 15s and 30s Merged stages 3 and 4 | Use data/SS3_filter_new Weighted loss function Modify architecture: Tweak depth (current: 32), # of heads (current: 8) Use n previous recognized stages as input Multiple channels input
Week of Oct. 9, 2023
Improved data processing script
  One-hot and scalar outputs
  Option to output unbiased dataset
  Visualization
Ran transformer prototype on various subset of data  Accuracy = ~75%
EngSci thesis: Sleep staging AI model design and ASIC implementation

## Slide 3
Metric | Edge TPU | CPU
Mean inference time (n = 2000) | 0.754ms | 2.706ms
Std. dev. inference time (n = 2000) | 0.038ms | 0.154ms
Week of Dec. 18, 2023
Got Coral USB Edge Accelerator to run model
Compared output w/ Tensorflow model on CPU for exactness
EngSci thesis: Sleep staging AI model design and ASIC implementation
*Inference on 30s clip (float32, 256Hz sampling, single-channel)

## Slide 4
Model finished: 82.3% @ 52k param. (but hyperparam. searching)
  15s @ 128Hz is also not too bad (80.8% @ 50k parameters)
ASIC architecture finished
Interim report submitted
C++ model of ASIC in progress (~50% done)
CMC access granted and synthesis flow works
SleepEDF-Expanded (downloaded in data/)
Got access to STAGES (1500 patients, ~400GB) and SHHS (~10000 nights, ~350GB)
  Can download them but will need to request more storage (we have 1TB)
EngSci thesis: Sleep staging AI model design and ASIC implementation
Notes: What area can I have?